C0VERTl’s Packet Sniffing Tutorial  121201 revised version

<< Drops the Sex Pistols in to my CD Player, select “Pretty Vacant”, then “EMI”..  Coffee - super black, no sugar, no cream. A smoke? Perhaps. Daylight creeping to my window. Rekindled love with my computer, fusion>>>

Ok, I guess I will start off with the basic overview of packets and computers.

A Packet.

In TCP/IP, Ethernet, and most other computer systems use packets. Packets can also be referred to as Frames or datagrams. But they are basically the same thing. Your email/file is broken down in to many little packets so you don’t clog the network and error correcting is easier.

In bare bones a packet or frame or datagram is this:

Sender IP:Sender Port--Designation IP:Designation Port

Session ID -- Packet Sequence # -- Error Checksum --

-- Data/ a part of the file that was sent --

<< If you don’t know what an IP is, or port then review TCP/IP here: “TCP/IP in 14 days” > http://c0vertl.tripod.com/dntext.htm >>>

When you send a packet, it has your IP on it, then it needs to tell the other computer what port it came from, its important as it tells what daemon/application the code can be translated by - it is not nessarily the return port.  You need the session ID, a special but hackable number that identifies the connection between the two computers. The Packet sequence number is important because your email/file was broken down in to many little packets , because your packets can take many paths to get to the designation, some packets will arrive later than others, out of sequence, so - the receiving computer has to reassemble your email or file. This also helps if your communication was corrupted - the designation computer can just request that only the missing packets be resent - rather than the entire file/message. TCP/IP Session Hijacking is another tutorial.

The idea of a packet or frame is that your file is broken down in to small packets or frames to be sent to the other computer on the network. Your files have to be broken down in to packets so you don't tie up the entire network bandwidth when you download a 12mb porn MPEG. The receiving puts all the packets together and organizes them by sequence numbers that are in the packets. Also because the packet has your IP number, a session ID, it can organise all the packets by sender and the session you are having with the sender - so you can do multiple downloads! ( I hate people that sit around waiting for a download - don't they understand MULTITASKING??? )

Did I repeat this enough for understanding?

Do not proceed past this point unless you understand the above about packets!

The Computer on the Ethernet/TCP/IP protocol

In normal mode, when you send a packet down the wire to another computer, the packet will be handled by each computer along the way.

Each computer will normally just look at the IP header and see if the IP matches theirs, if the packet is theirs, they recieve the packet and send an ACK to you that it was recieved. If the IP does not match the computer's, it does not continue to open the packet, and it stops doing anything with the packet.

This actually would take place with the network card because this action is operating at a low level of the network layer. Thats why your computer is not busy like that little green light on your NIC (network interface card)

When you install a packet sniffer on a computer, you have made it promiscuous (remember that slut back in school that would fuck anybody but you?) Promiscuous means that computer will now receive every packet just like it was designated for it!

Several things that make packet sniffing hard.

packetsniffers that do not decode the packets for you and display in an organised form so you can see send/rec IPs, MACs, protocol, ports, etc. make packet sniffing too time consuming. You need speed to effectively react to what is happening.

This is an example of what the data field of a packet can look like, now you can take a hex chart and decode each one by one…  or just have a program do it in a blink of an eye.

20 53 52 43 00 00 44 45 53 54 00 00 08 00 45 00 00 28 85 14 00 00 40 06 D9 DB 0C 57 38 0E 40 0C 97 6F 06 5C 00 50 00 46 F3 81 53 AD 6D 6C 50 10 21 80 B6 E6 00 00

Watching a packet sniffer even on ONE computer can look like you are trying to drink from a high-pressure firehose. The packet sniffer should have FILTERs so you can ignore unimportant normal traffic, or perhaps other unimportant computers, you will even see packets from your own IP.

The decoding part of the packet sniffer is VERY important, with IRIS  I  automatically have the packets decoded, so I can make real time decisions. Packets are actually data on a low level computer language - in hex, the packet does not actually get translated until it reached the Application level of the networking ‘tree’ (see OSI layers) See #2.

Conclusion: Get a good packet sniffer, time is critical to good packet sniffing tactics.

2. Just because you recieved the packet it does not mean you will be able to understand it! Remember those packets were designated for ports where the proper application is running to decode it! When you view the inside of the packet you are seeing only a part of the message/file and you are looking at raw, untranslated data.  So where it maybe easy to read a chat converstation from a sniffed Yahoochat!, it might be impossible to read a AOL chat - because the AOL packet needs to be decoded by the AOL software! Where the Yahoochat sends the data in plain-text. Encrypted packets, are just a regular packet except the data inside has to be decrypted by a browser or program. Encrypted 'Wrapped" Tcp/ip 'wrappers'  hide the actual packet by enclosing the orignal packet in another, the entire original packet is encrypted, making it even harder to crack network traffic (the IP will not be the target computer's IP) Can you replay a packet meant for AOL on another computer, yes, but you’ll need all the packets required to make it work, the scripting, the program commands, etc have to be done in proper sequence. Thats why most packet sniffers are run for the plain text data intrusion.

When you sniff packets, there is plenty of plain text data available. You can see what website page they are loading, you can catch the login when they send it out to the internet. Tripod/lycos is the worst - they will send your user/pass in plain text. Excite and Hotmail are good examples of cypher-text logins, your login is scrambled. Cookie attacks maybe possible, but you'll need a TCP/IP session hijack.

Here is an example of plain-text NFO you might see, this is from AIM:

Remember this is the hex code translated :

SRC..DEST....E...Y...@....W8.@..=.V.F.F..Z...P. j....*.U.................*.U..b.................{.......{.......{.......{.......{.......{...............{.......{................*.U.................<.c.<..7.................c0vert0ne....Windows 98..4.10.67766446..Intel Pentium.0Microsoft Corporation:BSD Socket API for Windows..4.10.1998............*.U...............*.U..............c0vert0ne*.U...................

So from the plain text leakage, I see a user name, mine : C0VERT0NE, it also leaked about my OS! With this you have enumerated one user account to look for, plus you can look for exploits for this specific OS!

Remember www.tripod.com has no encryption or coding to hide user and password? Read this packet below for my user and password! This is the plain text data found inside a packet send from my box during login for tripod.com:

SRC..DEST....E..@....@..O.W8......!.P.S..1M..P.!.Vk..GET /header??Z=676056&VID=7527&LHS=2&m_PR=26&LHM=1&LHL=1&LHS=2 HTTP/1.1..Accept: */*..Referer: http://ldbauth.lycos.com/cgi-bin/mayaLogin?m_PR=26&m_CBURL=http%3A%2F%2Fwww.tripod.lycos.com%2Fbin%2Fmembership%2Flogin%2F&m_CBERRURL=http%3A%2F%2Fwww.tripod.lycos.com%2Fbin%2Fmembership%2Flogin%2F&m_AID=0&m_TRURL=&m_APPID=0&m_LC=0&Z=1008166663&m_U=C0VERTl&m_P=bullshitpasswd&m_AS=1&m_WS=on..Accept-Language: en-us..Accept-Encoding: gzip, deflate..User-Agent: Mozilla/4.0 (compatible; MSIE 5.0; Windows 98; DigExt; AT&T WNS5.0)..Host: hb.lyce

If you view this packet in a html active page, you will see the URL in the packet become a hypertext link, if not , try this:

http://ldbauth.lycos.com/cgi-bin/mayaLogin?m_PR=26&m_CBURL=http%3A%2F%2Fwww.tripod.lycos.com%2Fbin%2Fmembership%2Flogin%2F&m_CBERRURL=http%3A%2F%2Fwww.tripod.lycos.com%2Fbin%2Fmembership%2Flogin%2F&m_AID=0&m_TRURL=&m_APPID=0&m_LC=0&Z=1008166663&m_U=C0VERTl&m_P=bullshitpasswd&m_AS=1&m_WS=on..Accept-Language:

This is an example of using data from a packet, if this had been an actual password, you would be logged in as C0VERTl!!!!!!

Yes, that is a bullshit password ; )  You can see this was the URL script that was inside the packet, the lack of URL encoding exposes the user ( U=C0VERTl ) and the password for his login ( P=bullshitpasswd ), again here more NFO is leaked about my OS and applications I am using.

I don’t have to know too much about tripod or the URL encoding , its obvious I have a user and password, you can use the same technique with other logins - as long as they do not encrypt the data inside the packet.

Use Filters, With IRIS I can set my filter for plain-text keywords like “User” , “U”, “Password”, “pass”, and “P”. It is also a good idea to filter out unimportant IPs, like yours, and normal traffic from devices ‘advertising’ there service/availability on the network, network broadcasts etc.  One minute of  packet sniffing on a small 2 node network can mean over 2000 packets to have to look through!! With filters you can at least narrow it down to 50. People are over whelmed with packet sniffing because they do not have patience to look through the packets, let alone try to decode each one.

Network technology is improving, so packet sniffing is harder. For packet sniffing you need to share the wire with other computers.  Active hubs can switch the packet traffic to specific computers at the hub level. What that means is the hub isolates the traffic to each computer, you will only see packets for your box. This is called switching, connections are made at the hub. Also, in big college campuses, corporations, the hub will at least break down the network in to different sections - payroll will be controlled by one switch or active hub, while you on the sales department network will not be able to see traffic from the payroll department section of the network, this is called segmentation. You will only be able to sniff packets on your segment, such as a class room, or company department. This can be defeated by installing a stealth packetsniffer on each segment of the network, each stealth program will work like a trojan, sending the packets back to your computer.

More Network technology, NICs can be made to be unable to sniff, or be promiscuous, so it may not work on some computers. Also some NOS can alert the sysadmin that a computer has gone promiscuous too, alerting the sysadmin to your IP.

Packet sniffers by the very nature of their packet collecting can trigger alarms by growing in file size, if you are on a large network or did not configure filters, the packet sniffer’s database will grow in size - this is a tip off of a possible trojan sniffer. Even if a good trojan sniffer compresses its database, a sysadmin could be alerted by this mystery file.

Trojan Packet sniffers, are usually client programs that only collect, compress, and encrypt the collection of its packets, it then sends the file to you, running the server side of the trojan program, which is the only program that can decode the file. If a sysadmin would find your client program, he/she will not be able to find NFO such as the IP of the server side (your box!) unless he/she had the admin program for the client, let a lone read the data that the trojan collected - because it is encrypted. Trojan packet sniffers can be detected by a trojan or AV programs. Sub7 and BO are two examples.

Legitimate uses of packet sniffers by a sysadmin:

Packet sniffers are actually called protocol analyzers. Sysadmins use these programs to look for bad packets on their network as well as looking for traffic problems, such as a bad NIC that is jabbering away garbage. You can also use it to determine what traffic is clogging up your segment, so you can plan routing.

A Security System admin like yourself, would use a packetsniffer to catch employees or students on your network that are using the network against rules. These programs can be used to collect evidence of what you do on the network, such as accessing computers and files you should not be, surfing for MP3s, or porn, as well as sending out sensitive company NFO. A packet is pretty hard evidence , it has your IP, your MAC, who you talked to, and what was in the data you sent.

Detecting  a computer in promiscuous mode is hard, as it is a passive scan - there is no broadcast - except if you use the client/server trojan packet sniffers - then a sysadmin could detect the client trying to communicate with the server side of the trojan. But some NOS can give the sysadmin reports on all the adapters (NICs) on the network and their status - it has to be special to the NOS, because you simply cannot determine if a computer is promisuous by pinging or sending it a packet.

Can you sniff packets off the Internet?

No, your ISP is your switch so you will not see traffic unless it is meant for your IP. If you did set up a router to include your computer or server as a part of the Internet - your computer will not likely be able to handle the traffic - proably over 2000 packets a second! This is what makes the FBI’s Carnivore technology useless - you need to filter for IPs and specific keywords. Packet sniffer is meant for small networks, or installed on a single computer - the traffic to and from that box. You might be able to sniff a cable network, if the cables in your neighborhood are set up as a bus network, and all of you are before a switch, you can sniff!

You can run a packet sniffer off a dial up computer, but again you are switched at the ISP, so you will only be able to analyze your packets - this is good enough for learning how to sniff and what programs leak plain-text NFO. I suggest this

Well, the music has stopped, and I am out of coffee, so the tut ends here.

Feel free to comment on this post If this post is a bit disorganized, oh well, its cause I am a hacker.

C0VERTl