IP Filter Based Firewalls HOWTO

Brendan Conoboy <synk@swcp.com>

Erik Fichtner <emf@obfuscation.org>

Sun May 14 15:20:08 EDT 2000

Abstract:  This document is intended to introduce a new

user to the IP Filter firewalling package and,  at  the

same  time,  teach  the user some basic fundamentals of

good firewall design.

1.  Introduction

IP Filter is a great little firewall package.  It  does

just   about   everything  other  free  firewalls  (ipfwadm,

ipchains, ipfw) do, but it's also  portable  and  does  neat

stuff  the  others don't.  This document is intended to make

some cohesive sense of the  sparse  documentation  presently

available  for ipfilter.  Some prior familiarity with packet

filtering will be useful, however too much  familiarity  may

make this document a waste of your time.  For greater under-

standing of firewalls, the authors reccomend reading  Build-

ing Internet Firewalls, Chapman & Zwicky, O'Reilly and Asso-

ciates; and TCP/IP Illustrated, Volume 1, Stevens,  Addison-

Wesley.

1.1.  Disclaimer

The  authors  of  this document are not responsible for

any damages incurred due to actions taken based on this doc-

ument. This document is meant as an introduction to building

a  firewall  based  on  IP-Filter.   If  you  do  not   feel

-2-

comfortable  taking responsibility for your own actions, you

should stop reading this document and hire a qualified secu-

rity professional to install your firewall for you.

1.2.  Copyright

Unless  otherwise  stated,  HOWTO  documents  are copy-

righted by their respective authors. HOWTO documents may  be

reproduced  and  distributed  in  whole  or  in part, in any

medium physical or electronic, as  long  as  this  copyright

notice  is retained on all copies. Commercial redistribution

is allowed and encouraged; however, the authors  would  like

to be notified of any such distributions.

All  translations, derivative works, or aggregate works

incorporating any HOWTO documents must be covered under this

copyright notice.  That is, you may not produce a derivative

work from a HOWTO and impose additional restrictions on  its

distribution. Exceptions to these rules may be granted under

certain conditions; please contact the HOWTO coordinator.

In short, we wish  to  promote  dissemination  of  this

information  through  as many channels as possible. However,

we do wish to retain copyright on the HOWTO  documents,  and

would  like  to be notified of any plans to redistribute the

HOWTOs.

1.3.  Where to obtain the important pieces

The     official     IPF      homepage      is      at:

<http://coombs.anu.edu.au/~avalon/ip-filter.html>

The  most  up-to-date  version  of this document can be

found at: <http://www.obfuscation.org/ipf/>

2.  Basic Firewalling

This section is designed to familiarize you with ipfil-

ter's  syntax, and firewall theory in general.  The features

discussed here are features you'll find in any good firewall

package.   This  section  will give you a good foundation to

make reading and understanding  the  advanced  section  very

easy.   It must be emphasized that this section alone is not

enough to build a good firewall, and that the advanced  sec-

tion  really  is  required  reading for anybody who wants to

build an effective security system.

-3-

2.1.  Config File Dynamics, Order and Precedence

IPF (IP Filter) has a config file (as opposed  to  say,

running  some  command  again  and again for each new rule).

The config file drips with Unix:  There's one rule per line,

the  "#" mark denotes a comment, and you can have a rule and

a comment  on  the  same  line.   Extraneous  whitespace  is

allowed, and is encouraged to keep the rules readable.

2.2.  Basic Rule Processing

The  rules  are  processed from top to bottom, each one

appended after another.  This quite simply means that if the

entirety of your config file is:

block in all

pass  in all

The computer sees it as:

block in all

pass  in all

Which is to say that when a packet comes in, the first thing

IPF applies is:

block in all

Should IPF deem it necessary to move on to the next rule, it

would then apply the second rule:

pass  in all

At  this  point,  you might want to ask yourself "would

IPF move on to the second rule?"  If  you're  familiar  with

ipfwadm  or  ipfw,  you  probably  won't  ask yourself this.

Shortly after, you will become bewildered at the  weird  way

packets  are  always  getting  denied  or  passed  when they

shouldn't.  Many packet filters stop  comparing  packets  to

rulesets  the moment the first match is made; IPF is not one

of them.

Unlike the other packet filters, IPF keeps  a  flag  on

whether  or  not  it's going to pass the packet.  Unless you

interrupt the flow, IPF will go through the entire  ruleset,

making  its  decision  on whether or not to pass or drop the

packet based on the last matching rule.  The scene: IP  Fil-

ter's  on  duty.   It's  been  been scheduled a slice of CPU

time.  It has a checkpoint clipboard that reads:

block in all

pass  in all

-4-

A packet comes in the interface and it's time to go to work.

It  takes a look at the packet, it takes a look at the first

rule:

block in all

"So far I think I will block  this  packet"  says  IPF.   It

takes a look at the second rule:

pass  in all

"So far I think I will pass this packet" says IPF.  It takes

a look at a third rule.  There is no third rule, so it  goes

with  what  its  last  motivation  was,  to  pass the packet

onward.

It's a good time to point out that even if the  ruleset  had

been

block in all

block in all

block in all

block in all

pass  in all

that  the packet would still have gone through.  There is no

cumulative effect.  The  last  matching  rule  always  takes

precedence.

2.3.  Controlling Rule Processing

If  you  have experience with other packet filters, you

may find this layout to be confusing, and you may be  specu-

lating  that  there are problems with portability with other

filters and speed of rule matching.  Imagine if you had  100

rules  and  most  of  the applicable ones were the first 10.

There would be a terrible overhead for every  packet  coming

in  to  go through 100 rules every time.  Fortunately, there

is a simple keyword you can add to any rule  that  makes  it

take action at that match.  That keyword is quick.

Here's  a  modified  copy  of the original ruleset using the

quick keyword:

block in quick all

pass  in       all

In this case, IPF looks at the first rule:

block in quick all

The packet matches and the search is over.   The  packet  is

expunged  without a peep.  There are no notices, no logs, no

memorial service.  Cake will not be served.  So  what  about

-5-

the next rule?

pass  in       all

This  rule is never encountered.  It could just as eas-

ily not be in the config file at all.  The sweeping match of

all  and  the  terminal keyword quick from the previous rule

make certain that no rules are followed afterward.

Having half a config file laid to  waste  is  rarely  a

desirable  state.   On  the other hand, IPF is here to block

packets and as configured,  it's  doing  a  very  good  job.

Nonetheless,  IPF  is also here to let some packets through,

so a change to the ruleset to make this possible  is  called

for.

2.4.  Basic filtering by IP address

IPF  will match packets on many criteria.  The one that

we most commonly think of is the IP address.  There are some

blocks of address space from which we should never get traf-

fic.  One such  block  is  from   the  unroutable  networks,

192.168.0.0/16 (/16 is the CIDR notation for a netmask.  You

may  be  more  familiar  with  the  dotted  decimal  format,

255.255.0.0.   IPF  accepts  both).   If you wanted to block

192.168.0.0/16, this is one way to do it:

block in quick from 192.168.0.0/16 to any

pass  in       all

Now we have a less  stringent  ruleset  that  actually  does

something  for  us.   Lets  imagine  a  packet comes in from

1.2.3.4.  The first rule is applied:

block in quick from 192.168.0.0/16 to any

The packet is from 1.2.3.4, not 192.168.*.*, so there is  no

match.  The second rule is applied:

pass  in       all

The  packet from 1.2.3.4 is definitely a part of all, so the

packet is sent to whatever it's destination happened to  be.

On  the other hand, suppose we have a packet that comes

in from 192.168.1.2.  The first rule is applied:

block in quick from 192.168.0.0/16 to any

There's a match, the packet is dropped, and that's the  end.

Again,  it doesn't move to the second rule because the first

rule matches and contains the quick keyword.

-6-

At this point you can build a fairly extensive  set  of

definitive  addresses  which  are  passed or blocked.  Since

we've already started blocking private  address  space  from

entering our firewall, lets take care of the rest of it:

block in quick from 192.168.0.0/16 to any

block in quick from 172.16.0.0/12 to any

block in quick from 10.0.0.0/8 to any

pass  in       all

The first three address blocks are the unroutable IP space.

2.5.  Controlling Your Interfaces

It seems very frequent  that  companies  have  internal

networks  before  they want a link to the outside world.  In

fact, it's probably reasonable to say that's the main reason

people  consider  firewalls in the first place.  The machine

that bridges the outside world to the inside world and  vice

versa  is  the  router.   What separates the router from any

other machine is simple: It has more than one interface.

Every packet you recieve comes from  a  network  inter-

face;  every  packet  you transmit goes out a network inter-

face.  Say your machine has 3  interfaces,  lo0  (loopback),

xl0  (3com  ethernet),  and  tun0  (FreeBSD's generic tunnel

interface that PPP uses), but you don't want packets  coming

in on the tun0 interface?

block in quick on tun0 all

pass  in               all

In  this case, the on keyword means that that data is coming

in on the named interface.  If a packet comes  in  on  tun0,

the  first  rule will block it.  If a packet comes in on lo0

or in on xl0, the first rule will not match, the second rule

will, the packet will be passed.

2.6.  Using IP Address and Interface Together

It's  an  odd state of affairs when one decides it best

to have the tun0 interface up, but not allow any data to  be

recieved  from  it.   The more criteria the firewall matches

against, the tighter (or looser) the  firewall  can  become.

Maybe  you want data from tun0, but not from 192.168.0.0/16?

This is the start of a powerful firewall.

block in quick on tun0 from 192.168.0.0/16 to any

pass  in       all

-----------

See             rfc1918            at

<http://www.faqs.org/rfcs/rfc1918.html>

-7-

Compare this to our previous rule:

block in quick from 192.168.0.0/16 to any

pass  in       all

The old way, all traffic from 192.168.0.0/16, regardless  of

interface,  was  completely  blocked.  The new way, using on

tun0 means that it's only blocked if it comes in on the tun0

interface.   If  a  packet arrived on the xl0 interface from

192.168.0.0/16, it would be passed.

At this point you can build a fairly extensive  set  of

definitive  addresses  which  are  passed or blocked.  Since

we've already started blocking private  address  space  from

entering tun0, lets take care of the rest of it:

block in quick on tun0 from 192.168.0.0/16 to any

block in quick on tun0 from 172.16.0.0/12 to any

block in quick on tun0 from 10.0.0.0/8 to any

block in quick on tun0 from 127.0.0.0/8 to any

pass  in       all

You've  already seen the first 3 blocks, but not the fourth.

The fourth is a largely  wasted  class-A  network  used  for

loopback.    Much   software  communicates  with  itself  on

127.0.0.1 so blocking it from an external source is  a  good

idea.

There's  a very important principle in packet filtering

which has only been alluded  to  with  the  private  network

blocking  and  that  is  this: When you know there's certain

types of data that only comes from certain places, you setup

the  system  to  only  allow  that  kind  of data from those

places.  In the case of the unroutable addresses,  you  know

that  nothing  from  10.0.0.0/8  should  be arriving on tun0

because you have no way to reply to it.  It's  an  illegiti-

mate  packet.   The  same  goes for the other unroutables as

well as 127.0.0.0/8.

Many pieces of software  do  all  their  authentication

based  upon  the  packet's originating IP address.  When you

have an internal network, say 20.20.20.0/24, you  know  that

the  only traffic for that internal network is going to come

off the local ethernet.  Should a packet from  20.20.20.0/24

arrive  over a PPP dialup, it's perfectly reasonable to drop

it on the floor, or put it in a dark room for interrogation.

It  should by no means be allowed to get to its final desti-

nation.  You can accomplish this  particularly  easily  with

what you already know of IPF.  The new ruleset would be:

block in quick on tun0 from 192.168.0.0/16 to any

block in quick on tun0 from 172.16.0.0/12 to any

block in quick on tun0 from 10.0.0.0/8 to any

block in quick on tun0 from 127.0.0.0/8 to any

-8-

block in quick on tun0 from 20.20.20.0/24 to any

pass  in       all

2.7.  Bi-Directional Filtering; The "out" Keyword

So far, we've been passing or blocking inbound traffic.

There's been an implied pass out all that may or may not  be

desirable.  Just as you may pass and block incoming traffic,

you may do the same with outgoing traffic.  One possible use

of  this  idea  is to keep spoofed packets from exiting your

own network.  Instead of passing any traffic out the router,

you  could instead limit permitted traffic to packets origi-

nating at 20.20.20.0/24.  You might do it like this:

pass  out quick on tun0 from 20.20.20.0/24 to any

block out quick on tun0 from any to any

If a packet comes from 20.20.20.1/32, it gets  sent  out  by

the  first  rule.  If a packet comes from 1.2.3.4/32 it gets

blocked by the second.

You can also make  similar  rules  for  the  unroutable

addresses.   If some machine tries to route a packet through

IPF with a destination in 192.168.0.0/16, why not  drop  it?

The worst that can happen is that you'll spare yourself some

bandwidth:

block out quick on tun0 from any to 192.168.0.0/16

block out quick on tun0 from any to 172.16.0.0/12

block out quick on tun0 from any to 10.0.0.0/8

In the narrowest viewpoint, this doesn't enhance your  secu-

rity.   It  enhances everybody else's security, and that's a

nice thing to do.  As another viewpoint, one  might  suppose

that because nobody can send spoofed packets from your site,

that your site has less value as a relay for  crackers,  and

as such is less of a target.

2.8.  Logging What Happens; The "log" Keyword

Up  to  this point, all blocked and passed packets have

been silently blocked and silently passed.  Usually you want

to  know if you're being attacked rather than wonder if that

firewall is really buying you any added benefits.   While  I

wouldn't  want to log every passed packet, and in some cases

every blocked packet, I would want to know about the blocked

packets from 20.20.20.0/24.  To do this, we add the log key-

word:

block in     quick on tun0 from 192.168.0.0/16 to any

-----------

This can, of course, be changed by using -DIPFIL-

TER_DEFAULT_BLOCK  when compiling ipfilter on your

system.

-9-

block in     quick on tun0 from 172.16.0.0/12 to any

block in     quick on tun0 from 10.0.0.0/8 to any

block in     quick on tun0 from 127.0.0.0/8 to any

block in log quick on tun0 from 20.20.20.0/24 to any

pass  in       all

So far, our firewall is pretty good at blocking packets com-

ing  to it from suspect places, but there's still more to be

done.  For one thing, we're accepting packets destined  any-

where.   One  thing  we  ought to do is make sure packets to

20.20.20.0/32 and 20.20.20.255/32 get dropped on the  floor.

To  do  otherwise  opens  the  internal  network for a smurf

attack.  These two lines would prevent our hypothetical net-

work from being used as a smurf relay:

block in log quick on tun0 from any to 20.20.20.0/32

block in log quick on tun0 from any to 20.20.20.255/32

This brings our total ruleset to look something like this:

block in     quick on tun0 from 192.168.0.0/16 to any

block in     quick on tun0 from 172.16.0.0/12 to any

block in     quick on tun0 from 10.0.0.0/8 to any

block in     quick on tun0 from 127.0.0.0/8 to any

block in log quick on tun0 from 20.20.20.0/24 to any

block in log quick on tun0 from any to 20.20.20.0/32

block in log quick on tun0 from any to 20.20.20.255/32

pass  in       all

2.9.  Complete Bi-Directional Filtering By Interface

So  far  we have only presented fragments of a complete

ruleset.  When you're actually creating  your  ruleset,  you

should  setup rules for every direction and every interface.

The default state of ipfilter is to pass packets.  It is  as

though  there  were an invisible rule at the beginning which

states pass in all and pass out all.  Rather  than  rely  on

some  default behaviour, make everything as specific as pos-

sible, interface by interface, until every base is  covered.

First  we'll  start with the lo0 interface, which wants

to run wild and free.  Since these are programs  talking  to

other  on  the  local  system,  go  ahead  and keep it unre-

stricted:

pass out quick on lo0

pass in  quick on lo0

Next, there's the xl0 interface.  Later on we'll begin plac-

ing  restrictions  on  the xl0 interface, but to start with,

we'll act as though  everything  on  our  local  network  is

trustworthy and give it much the same treatment as lo0:

pass out quick on xl0

-10-

pass in  quick on xl0

Finally,  there's the tun0 interface, which we've been half-

filtering with up until now:

block out quick on tun0 from any to 192.168.0.0/16

block out quick on tun0 from any to 172.16.0.0/12

block out quick on tun0 from any to 10.0.0.0/8

pass  out quick on tun0 from 20.20.20.0/24 to any

block out quick on tun0 from any to any

block in     quick on tun0 from 192.168.0.0/16 to any

block in     quick on tun0 from 172.16.0.0/12 to any

block in     quick on tun0 from 10.0.0.0/8 to any

block in     quick on tun0 from 127.0.0.0/8 to any

block in log quick on tun0 from 20.20.20.0/24 to any

block in log quick on tun0 from any to 20.20.20.0/32

block in log quick on tun0 from any to 20.20.20.255/32

pass  in     all

This is a pretty significant amount  of  filtering  already,

protecting  20.20.20.0/24  from  being spoofed or being used

for spoofing.  Future examples will continue  to  show  one-

sideness, but keep in mind that it's for brevity's sake, and

when setting up your own ruleset,  adding  rules  for  every

direction and every interface is necessary.

2.10.  Controlling Specific Protocols; The "proto" Keyword

Denial  of  Service  attacks  are  as rampant as buffer

overflow exploits.  Many denial of service attacks  rely  on

glitches  in  the  OS's  TCP/IP stack.  Frequently, this has

come in the form  of  ICMP  packets.   Why  not  block  them

entirely?

block in log quick on tun0 proto icmp from any to any

Now  any ICMP traffic coming in from tun0 will be logged and

discarded.

2.11.  Filtering ICMP with the "icmp-type" Keyword;  Merging

Rulesets

Of course, dropping all ICMP isn't really an ideal sit-

uation.  Why not drop all ICMP?  Well, because  it's  useful

to  have  partially enabled.  So maybe you want to keep some

types of ICMP traffic and drop other  kinds.   If  you  want

ping and traceroute to work, you need to let in ICMP types 0

and 11.  Strictly speaking, this might not be a  good  idea,

but  if  you need to weigh security against convenience, IPF

lets you do it.

pass in quick on tun0 proto icmp from any to 20.20.20.0/24 icmp-type 0

-11-

pass in quick on tun0 proto icmp from any to 20.20.20.0/24 icmp-type 11

Remember that ruleset order is important.  Since we're doing

everything  quick we must have our passes before our blocks,

so we really want the last three rules in this order:

pass  in     quick on tun0 proto icmp from any to 20.20.20.0/24 icmp-type 0

pass  in     quick on tun0 proto icmp from any to 20.20.20.0/24 icmp-type 11

block in log quick on tun0 proto icmp from any to any

Adding these 3 rules to the anti-spoofing  rules  is  a  bit

tricky.  One error might be to put the new ICMP rules at the

beginning:

pass  in     quick on tun0 proto icmp from any to 20.20.20.0/24 icmp-type 0

pass  in     quick on tun0 proto icmp from any to 20.20.20.0/24 icmp-type 11

block in log quick on tun0 proto icmp from any to any

block in     quick on tun0 from 192.168.0.0/16 to any

block in     quick on tun0 from 172.16.0.0/12 to any

block in     quick on tun0 from 10.0.0.0/8 to any

block in     quick on tun0 from 127.0.0.0/8 to any

block in log quick on tun0 from 20.20.20.0/24 to any

block in log quick on tun0 from any to 20.20.20.0/32

block in log quick on tun0 from any to 20.20.20.255/32

pass  in       all

The problem with this is that an ICMP  type  0  packet  from

192.168.0.0/16  will get passed by the first rule, and never

blocked by the fourth rule.  Also, since we quickly pass  an

ICMP ECHO_REPLY (type 0) to 20.20.20.0/24, we've just opened

ourselves back up to a  nasty  smurf  attack  and  nullified

those  last two block rules.  Oops.  To avoid this, we place

the ICMP rules after the anti-spoofing rules:

block in     quick on tun0 from 192.168.0.0/16 to any

block in     quick on tun0 from 172.16.0.0/12 to any

block in     quick on tun0 from 10.0.0.0/8 to any

block in     quick on tun0 from 127.0.0.0/8 to any

block in log quick on tun0 from 20.20.20.0/24 to any

block in log quick on tun0 from any to 20.20.20.0/32

block in log quick on tun0 from any to 20.20.20.255/32

pass  in     quick on tun0 proto icmp from any to 20.20.20.0/24 icmp-type 0

pass  in     quick on tun0 proto icmp from any to 20.20.20.0/24 icmp-type 11

block in log quick on tun0 proto icmp from any to any

pass  in       all

Because we block spoofed traffic before the ICMP  rules  are

processed, a spoofed packet never makes it to the ICMP rule-

set.  It's very important to keep such  situations  in  mind

when merging rules.

-12-

2.12.  TCP and UDP Ports; The "port" Keyword

Now that we've started blocking packets based on proto-

col, we can start blocking packets based on specific aspects

of each protocol.  The most frequently used of these aspects

is the port number.  Services such as rsh, rlogin, and  tel-

net  are  all  very  convenient  to have, but also hideously

insecure against network sniffing and spoofing.   One  great

compromise  is to only allow the services to run internally,

then block them externally.  This  is  easy  to  do  because

rlogin,  rsh,  and  telnet use specific TCP ports (513, 514,

and 23 respectively).  As such, creating rules to block them

is easy:

block in log quick on tun0 proto tcp from any to 20.20.20.0/24 port = 513

block in log quick on tun0 proto tcp from any to 20.20.20.0/24 port = 514

block in log quick on tun0 proto tcp from any to 20.20.20.0/24 port = 23

Make  sure  all  3 are before the pass in all and they'll be

closed off  from  the  outside  (leaving  out  spoofing  for

brevity's sake):

pass  in     quick on tun0 proto icmp from any to 20.20.20.0/24 icmp-type 0

pass  in     quick on tun0 proto icmp from any to 20.20.20.0/24 icmp-type 11

block in log quick on tun0 proto icmp from any to any

block in log quick on tun0 proto tcp from any to 20.20.20.0/24 port = 513

block in log quick on tun0 proto tcp from any to 20.20.20.0/24 port = 514

block in log quick on tun0 proto tcp from any to 20.20.20.0/24 port = 23

pass  in     all

You  might  also  want to block 514/udp (syslog),  111/tcp &

111/udp (portmap),  515/tcp  (lpd),  2049/tcp  and  2049/udp

(NFS), 6000/tcp (X11) and so on and so forth.  You can get a

complete listing of the ports being  listened  to  by  using

netstat -a (or lsof -i, if you have it installed).

Blocking  UDP  instead  of  TCP only requires replacing

proto tcp with proto udp.  The rule for syslog would be:

block in log quick on tun0 proto udp from any to 20.20.20.0/24 port = 514

IPF also has a shorthand way to write rules  that  apply  to

both  proto  tcp  and  proto  udp  at the same time, such as

portmap or NFS.  The rule for portmap would be:

block in log quick on tun0 proto tcp/udp from any to 20.20.20.0/24 port = 111

3.  Advanced Firewalling Introduction

This section is designed as an  immediate  followup  to

the  basic  section.   Contained below are both concepts for

-13-

advanced firewall design, and  advanced  features  contained

only  within  ipfilter.   Once you are comfortable with this

section, you should be able to build a very strong firewall.

3.1.  Rampant Paranoia; or The Default-Deny Stance

There's  a  big  problem  with blocking services by the

port: sometimes they move.  RPC based programs are  terrible

about  this,  lockd,  statd,  even nfsd listens places other

than 2049.  It's awfully hard to predict, and even worse  to

automate  adjusting  all  the time.  What if you miss a ser-

vice?  Instead of dealing with all that hassle,  lets  start

over  with  a  clean  slate.  The current ruleset looks like

this:

Yes, we really are starting over.  The first rule we're

going to use is this:

block in all

No  network  traffic gets through. None. Not a peep.  You're

rather secure with this setup.   Not  terribly  useful,  but

quite  secure.  The great thing is that it doesn't take much

more to make your box rather secure, yet useful  too.   Lets

say  the machine this is running on is a web server, nothing

more, nothing less.  It doesn't even  do  DNS  lookups.   It

just  wants to take connections on 80/tcp and that's it.  We

can do that.  We can do that with a  second  rule,  and  you

already know how:

block in       on tun0 all

pass  in quick on tun0 proto tcp from any to 20.20.20.1/32 port = 80

This  machine  will  pass in port 80 traffic for 20.20.20.1,

and deny everything else.  Perhaps this is all one needs?

3.2.  Implicit Allow; The "keep state" Rule

Well, we usually find ourselves needing more.  We  want

to  be  able to telnet out over the tun0 interface.  We want

convenience and security in one.  Lots of  people  seem  to,

that's  why  ciscos  have  an "established" clause that lets

established tcp sessions go through.  Ipfw has  established.

Ipfwadm  has setup/established.  They all have this feature,

but the name is very misleading.

When we first saw it, we thought it  meant  our  packet

filter  was keeping track of what was going on, that it knew

if a connection was really established or not.  The fact is,

they're  all  taking  the  packet's word for it.  That's why

they only support established TCP  connections,  that's  the

-14-

only  protocol  that has flags which the router can extrapo-

late the established state of the connection.   Anybody  who

can create a packet with bogus flags can get by such a fire-

wall.

Where does IPF come in to play here,  you  ask?   Well,

unlike  the  other  firewalls,  IPF really can keep track of

whether or not a connection is established.  And it'll do it

with  UDP and ICMP, not just TCP.  The only problem is this:

the way it does it is non-intuitive.  Ipf calls  it  keeping

state.  The keyword for the ruleset is keep state.

Keep  state's  setup  is weird.  Normally, we know that

when we want a packet to come in, we used pass in  and  when

we  want  a  packet coming in to be blocked we use block in.

State is different in that, if you want a packet to come in,

you  say  pass  out, and if you want a packet to go out, you

say pass in  By passing the packet with state in one  direc-

tion  ,  a reciprocal rule is created that allows a reply to

come back in the other direction.   Lets  show  this  as  an

actual rule:

pass out quick proto tcp from 20.20.20.1/32 to any keep state

Though  it  doesn't  say so, you must imagine there being an

auxiliary rule that exists in the same place  in  line  that

reads:

pass in quick proto tcp With State to 20.20.20.1/32

There is no way to express the previous line, don't even try

putting it in there, it won't work.  The keep  state  option

in the pass out rule makes it implicit.

Here's what our ruleset looks like now:

block in       on tun0

pass out quick on tun0 proto tcp from 20.20.20.1/32 to any keep state

pass  in quick on tun0 proto tcp from any to 20.20.20.1/32 port = 80

The  workings  of  the  keep  state ruleset is much like the

workings of the saying "do not speak until spoken to."  It's

just not permitted (except on port 80).  Actually, lets keep

state on UDP and ICMP packets as well:

block in       on tun0

pass out quick on tun0 proto tcp/udp from 20.20.20.1/32 to any keep state

pass out quick on tun0 proto icmp    from 20.20.20.1/32 to any keep state

pass  in quick on tun0 proto tcp from any to 20.20.20.1/32 port = 80

Now we're keeping state on TCP, UDP, ICMP.  Now we can  make

outgoing  connections  as though there's no firewall at all,

yet would-be attackers can't get  back  in.   This  is  very

handy because there's no need to track down what ports we're

-15-

listening to, only the ports we want people to  be  able  to

get to.

Please  note  that  you  must  keep state from the very

first packet of a potential connection.  For example, if  we

have a set of rules that looks like this:

pass in quick on tun0 proto tcp from any to 20.20.20.1/32 port = 23 flags S

pass out quick on tun0 proto tcp from any to any keep state

At  first  glance, this set of rules looks pretty good. It's

filtering such that it's only allowing SYN packets  to  come

in  from  the  outside to our telnet port, and we're keeping

state on outbound connections.  This is pretty  good.   But,

what  happens  here is that the SYN packet comes through the

firewall just fine and tickles the telnet daemon.   The  tcp

stack  in  the  kernel  then  replies with a SYN-ACK packet,

which passes through the firewall.  The firewall  says  "New

connection! Time to keep state!" and sets up an entry in the

state table.  The telnet client end's tcp stack then replies

with an ACK packet, thus completing the three-way handshake.

Only the firewall has only seen  the  last  two  packets  to

record  in  the state table.  The firewall is confused.   It

will default to sitting around for 60  seconds  waiting  for

the three-way to complete successfully (and send the connec-

tion into what IPF calls 4/4 mode,  which  you  can  see  by

using ipfstat -s to examine the state table).   But from the

point of view of IP Filter,  the  three-way  handshake  will

never  complete.  So you have exactly 60 seconds to actually

do anything in your  telnet  session.   Well,  not  exactly.

See,  every  subsequent  ACK  packet that the server replies

with will reset this counter back to 60 seconds. (which will

be  one  ACK  packet  for  every  packet transmitted.  In an

interactive session, this is typically one for every  letter

you  type. Usually.)  So you really have 60 seconds from the

time you stop typing before the incomplete  state  entry  is

torn  down.   Since  we're  only letting SYN packets through

unmolested, and you're now in the middle of  an  interactive

session  and  only sending ACK packets, you'll find that you

can no longer type anything.   Unless the server end happens

to  say something to you first, and then you have another 60

seconds to play.

The moral of the story is,  keep  state  on  the  first

packet of a potential connection, if you're like us and want

to rely on state to keep your rules small.  Use  rules  like

this:

pass in quick on tun0 proto tcp from any to 20.20.20.1/32 port = 23 flags S keep state

pass out quick on tun0 proto tcp from any to any keep state

-16-

3.3.  Stateful Guts

Lets  take  a look at what happens, rule by rule, if we

use nslookup to get the IP address of www.3com.com:

$ nslookup www.3com.com

A DNS packet is generated:

17:54:25.499852 20.20.20.1.2111 > 198.41.0.5.53: 51979+

The packet is  from  20.20.20.1,  port  2111,  destined  for

198.41.0.5, port 53.  If a packet comes back from 198.41.0.5

port 53 destined for 20.20.20.1 port  2111  within  a  short

period  of time, the reply packet will be let through.  Mil-

liseconds later:

17:54:25.501209 198.41.0.5.53 > 20.20.20.1.2111: 51979 q: www.3com.com

The reply packet matches  the  state  criteria  and  is  let

through.   At  that  same moment that packet is let through,

the state gateway is closed and no new incoming packets will

be allowed in, even if they claim to be from the same place.

3.4.  FIN Scan Detection; "flags" Keyword, "keep frags" Key-

word

Lets go back to the 3 rule set:

block in       on tun0

pass out quick on tun0 proto tcp from 20.20.20.1/32 to any keep state

pass  in quick on tun0 proto tcp from any to 20.20.20.1/32 port = 80

As  it stands, anybody can connect to port 80.  That's good,

that's what it's there for in the first place.  However,  we

still have the problem with incomplete state entries that we

demonstrated earlier, although since this  firewall  accepts

any  packets  to port 80, your sessions won't be killed off,

but this will muck up your state table. This rule set should

read:

block in       on tun0

pass out quick on tun0 proto tcp from 20.20.20.1/32 port = 80 to any

pass out quick on tun0 proto tcp from 20.20.20.1/32 to any keep state

pass  in quick on tun0 proto tcp from any to 20.20.20.1/32 port = 80

This  way, we can ensure that we pass the packets that we're

not keeping state on without giving them a chance  to  dirty

up our state table.

We  can still make the system a little tighter.  When a

TCP session begins, there is a  certain  type  of  handshake

that takes place between the two machines.  The first packet

of the handshake has a unique set of flags that is only used

-17-

in the initialization of a TCP session.  Since we're keeping

state on every reply, the only kind of TCP packet to port 80

we  really  need  to pass in is that first handshake packet.

To do this, we use the flags option:

pass in quick on tun0 proto tcp from any to 20.20.20.1/32 port = 80 flags S

Now  all  incoming packets must either be handshakes or have

state already.  If anything else comes in, it's  probably  a

port  scan  or  a  forged  packet.  There's one exception to

that, which is when a packet comes in that's fragmented from

its  journey.  IPF has provisions for this as well, the keep

frags keyword.  With it, IPF will notice and keep  track  of

packets that are fragmented, allowing the expected fragments

to to go through.  Lets rewrite the 3 rules to log forgeries

and allow fragments:

block in log   on tun0

pass out quick on tun0 proto tcp from 20.20.20.1/32 to any keep state

pass  in quick on tun0 proto tcp from any to 20.20.20.1/32 port = 80 flags S keep state keep frags

The  reason  this  works is because the first reply, even in

the handshake phase, has state kept.  As  such,  all  subse-

quent  packets,  even  though they aren't handshake packets,

still make it through because the state  code  has  made  an

exception  for  them.   In  TCP  there  is  an ACK for every

packet, so the two machines may always send packets back and

forth, even out of turn.  The only scan this won't detect is

a SYN scan itself.  If you're truely worried about that, you

might even want to log all initial SYN packets.

3.5.  Responding To a Blocked Packet

So  far, all of our blocked packets have been dumped on

the floor, logged or not, we've never sent anything back  to

the  originating host.  Sometimes this isn't the most desir-

able of responses because in doing so, we actually tell  the

attacker  that  a  packet filter is present.  It seems a far

better thing to misguide the attacker into  believing  that,

while  there's no packet filter running, there's likewise no

services to break into.   This  is  where  fancier  blocking

comes into play.

-----------

Some examples use flags S/SA instead of flags  S.

flags  S  actually  equates  to flags S/AUPRFS and

matches against only the SYN packet out of all six

possible  flags, while flags S/SA will allow pack-

ets that may or may not have the URG, PSH, FIN, or

RST  flags  set.  Some protocols demand the URG or

PSH flags, and S/SAFR would be a better choice for

these,  however  we feel that it is less secure to

blindly use S/SA when it isn't required.  But it's

your firewall.

-18-

When  a service isn't running on a Unix system, it nor-

mally lets the remote host know with  some  sort  of  return

packet.   In  TCP,  this is done with an RST (Reset) packet.

When blocking a TCP packet, IPF can actually return  an  RST

to the origin by using the return-rst keyword.

Where once we did:

block in log on tun0 proto tcp from any to 20.20.20.0/24 port = 23

pass  in     all

We might now do:

block return-rst in log from any to 20.20.20.0/24 proto tcp port = 23

block in log quick on tun0

pass  in     all

We  need  two  block  statements since return-rst only works

with TCP, and we still want to block protocols such as  UDP,

ICMP,  and  others.   Now that this is done, the remote side

will get "connection refused" instead of  "connection  timed

out".

It's  also possible to send an error message when some-

body sends a packet to a UDP port on your  system.   Whereas

once you might have used:

block in log quick on tun0 proto udp from any to 20.20.20.0/24 port = 111

You  could  instead  use  the  return-icmp keyword to send a

reply:

block return-icmp(port-unr) in log quick on tun0 proto udp from any to 20.20.20.0/24 port = 111

According to TCP/IP  Illustrated,  port-unreachable  is  the

correct  ICMP type to return when no service is listening on

the port in question.  You can use any ICMP type  you  like,

but  port-unreachable  is probably your best bet.  It's also

the default ICMP type for return-icmp.

However, when using  return-icmp,  you'll  notice  that

it's  not very stealthy, and it returns the ICMP packet with

the IP address of the firewall, not the original destination

of  the  packet.   This was fixed in ipfilter 3.3, and a new

keyword; return-icmp-as-dest, has been added.   The new for-

mat is:

block return-icmp-as-dest(port-unr) in log on tun0 proto udp from any to 20.20.20.0/24 port = 111

3.6.  Fancy Logging Techniques

It  is  important  to note that the presence of the log

keyword only ensures that the packet will  be  available  to

the   ipfilter  logging  device;  /dev/ipl.    In  order  to

-19-

actually see this log information, one must be  running  the

ipmon  utility  (or  some  other  utility  that  reads  from

/dev/ipl).  The typical usage of log is coupled  with  ipmon

-s  to  log  the information to syslog.  As of ipfilter 3.3,

one can now even control the logging behavior of  syslog  by

using log level keywords, as in rules such as this:

block in log level auth.info quick on tun0 from 20.20.20.0/24 to any

block in log level auth.alert quick on tun0 proto tcp from any to 20.20.20.0/24 port = 21

In  addition  to  this,  you  can tailor what information is

being logged.  For example, you may not be  interested  that

someone  attempted  to probe your telnet port 500 times, but

you are interested that they probed you once.  You  can  use

the  log  first  keyword  to only log the first example of a

blocked packet.    We  find  this  behavior  detrimental  to

effective logging, but it may suit someone's purposes.

Another  useful  thing  you  can do with the logs is to

keep track of interesting pieces of the packet  in  addition

to  the  header information normally being logged.  Ipfilter

will give you the first 128 bytes of the packet if  you  use

the log body keyword.  You should limit the use of body log-

ging, as it makes your logs very verbose,  but  for  certain

applications,  it  is  often handy to be able to go back and

take a look at the packet, or to send this data  to  another

application that can examine it further.

3.7.  Putting It All Together

So  now  we  have  a  pretty tight firewall, but it can

still be tighter.  Some of the  original  ruleset  we  wiped

clean  is  actually  very useful.  I'd suggest bringing back

all the anti-spoofing stuff.  This leaves us with:

block in           on tun0

block in     quick on tun0 from 192.168.0.0/16 to any

block in     quick on tun0 from 172.16.0.0/12 to any

block in     quick on tun0 from 10.0.0.0/8 to any

block in     quick on tun0 from 127.0.0.0/8 to any

block in log quick on tun0 from 20.20.20.0/24 to any

block in log quick on tun0 from any to 20.20.20.0/32

block in log quick on tun0 from any to 20.20.20.255/32

pass  out quick on tun0 proto tcp/udp from 20.20.20.1/32 to any keep state

pass  out quick on tun0 proto icmp    from 20.20.20.1/32 to any keep state

pass  in  quick on tun0 proto tcp from any to 20.20.20.1/32 port = 80 flags S keep state

3.8.  Improving Performance With Rule Groups

Let's extend our use of our firewall by creating a much

more  complicated,  and  we hope more applicable to the real

world, example configuration For this example,  we're  going

to  change  the interface names, and network numbers.  Let's

assume that we have three interfaces in  our  firewall  with

-20-

interfaces xl0, xl1, and xl2.

xl0 is connected to our external network 20.20.20.0/26

xl1 is connected to our "DMZ" network 20.20.20.64/26

xl2 is connected to our protected network 20.20.20.128/25

We'll  define the entire ruleset in one swoop, since we fig-

ure that you can read these rules by now:

block in     quick on xl0 from 192.168.0.0/16 to any

block in     quick on xl0 from 172.16.0.0/12 to any

block in     quick on xl0 from 10.0.0.0/8 to any

block in     quick on xl0 from 127.0.0.0/8 to any

block in log quick on xl0 from 20.20.20.0/24 to any

block in log quick on xl0 from any to 20.20.20.0/32

block in log quick on xl0 from any to 20.20.20.63/32

block in log quick on xl0 from any to 20.20.20.64/32

block in log quick on xl0 from any to 20.20.20.127/32

block in log quick on xl0 from any to 20.20.20.128/32

block in log quick on xl0 from any to 20.20.20.255/32

pass out on xl0 all

pass out quick on xl1 proto tcp from any to 20.20.20.64/26 port = 80 flags S keep state

pass out quick on xl1 proto tcp from any to 20.20.20.64/26 port = 21 flags S keep state

pass out quick on xl1 proto tcp from any to 20.20.20.64/26 port = 20 flags S keep state

pass out quick on xl1 proto tcp from any to 20.20.20.65/32 port = 53 flags S keep state

pass out quick on xl1 proto udp from any to 20.20.20.65/32 port = 53 keep state

pass out quick on xl1 proto tcp from any to 20.20.20.66/32 port = 53 flags S keep state

pass out quick on xl1 proto udp from any to 20.20.20.66/32 port = 53 keep state

block out on xl1 all

pass in quick on xl1 proto tcp/udp from 20.20.20.64/26 to any keep state

block out on xl2 all

pass in quick on xl2 proto tcp/udp from 20.20.20.128/25 to any keep state

From this arbitarary example, we can already  see  that  our

ruleset is becoming unwieldy.   To make matters worse, as we

add more specific rules to our DMZ  network,  we  add  addi-

tional  tests  that  must  be parsed for every packet, which

affects the performance of the xl0 <-> xl2 connections.   If

you set up a firewall with a ruleset like this, and you have

lots of bandwidth and a moderate  amount  of  cpu,  everyone

that  has  a workstation on the xl2 network is going to come

looking for your head to place on a platter.   So,  to  keep

your  head  <->  torso  network intact, you can speed things

along by creating rule groups.   Rule groups  allow  you  to

write your ruleset in a tree fashion, instead of as a linear

list, so that if your packet has nothing to do with the  set

of  tests  (say, all those xl1 rules) those rules will never

be consulted.  It's somewhat like having multiple  firewalls

all on the same machine.

Here's a simple example to get us started:

-21-

block out quick on xl1 all head 10

pass out quick proto tcp from any to 20.20.20.64/26 port = 80 flags S keep state group 10

block out on xl2 all

In  this  simplistic example, we can see a small hint of the

power of the rule group.  If the packet is not destined  for

xl1,  the  head of rule group 10 will not match, and we will

go on with our tests.  If the packet does match for xl1, the

quick  keyword  will short-circuit all further processing at

the root level (rule group 0),  and  focus  the  testing  on

rules  which  belong  to group 10; namely, the SYN check for

80/tcp.  In this way, we can re-write  the  above  rules  so

that we can maximize performance of our firewall.

block in quick on xl0 head 1

block in     quick on xl0 from 192.168.0.0/16 to any  group 1

block in     quick on xl0 from 172.16.0.0/12 to any   group 1

block in     quick on xl0 from 10.0.0.0/8 to any      group 1

block in     quick on xl0 from 127.0.0.0/8 to any     group 1

block in log quick on xl0 from 20.20.20.0/24 to any   group 1

block in log quick on xl0 from any to 20.20.20.0/32   group 1

block in log quick on xl0 from any to 20.20.20.63/32  group 1

block in log quick on xl0 from any to 20.20.20.64/32  group 1

block in log quick on xl0 from any to 20.20.20.127/32 group 1

block in log quick on xl0 from any to 20.20.20.128/32 group 1

block in log quick on xl0 from any to 20.20.20.255/32 group 1

pass  in           on xl0 all group 1

pass out on xl0 all

block out quick on xl1 all head 10

pass out quick on xl1 proto tcp from any to 20.20.20.64/26 port = 80 flags S keep state group 10

pass out quick on xl1 proto tcp from any to 20.20.20.64/26 port = 21 flags S keep state group 10

pass out quick on xl1 proto tcp from any to 20.20.20.64/26 port = 20 flags S keep state group 10

pass out quick on xl1 proto tcp from any to 20.20.20.65/32 port = 53 flags S keep state group 10

pass out quick on xl1 proto udp from any to 20.20.20.65/32 port = 53         keep state group 10

pass out quick on xl1 proto tcp from any to 20.20.20.66/32 port = 53 flags S keep state

pass out quick on xl1 proto udp from any to 20.20.20.66/32 port = 53         keep state group 10

pass in quick on xl1 proto tcp/udp from 20.20.20.64/26 to any keep state

block out on xl2 all

pass in quick on xl2 proto tcp/udp from 20.20.20.128/25 to any keep state

Now  you  can  see the rule groups in action.  For a host on

the xl2 network, we can completely bypass all the checks  in

group  10  when  we're  not communicating with hosts on that

network.

Depending on your situation, it may be prudent to group

your  rules  by protocol, or various machines, or netblocks,

or whatever makes it flow smoothly.

-22-

3.9.  "Fastroute"; The Keyword of Stealthiness

Even though we're forwarding some packets, and blocking

other  packets, we're typically behaving like a well behaved

router should by decrementing the  TTL  on  the  packet  and

acknowledging  to  the entire world that yes, there is a hop

here.  But we can hide our presence from inquisitive  appli-

cations  like  unix  traceroute  which uses UDP packets with

various TTL values to map the hops between two sites.  If we

want  incoming  traceroutes  to  work, but we do not want to

announce the presence of our firewall as a hop, we can do so

with a rule like this:

block in quick on xl0 fastroute proto udp from any to any port 33434 >< 33465

The  presence  of the fastroute keyword will signal ipfilter

to not pass the packet into the Unix IP  stack  for  routing

which results in a TTL decrement.  The packet will be placed

gently on the output interface by  ipfilter  itself  and  no

such decrement will happen.  Ipfilter will of course use the

system's routing table to figure out  what  the  appropriate

output  interface  really  is,  but it will take care of the

actual task of routing itself.

There's a reason we used block quick  in  our  example,

too.   If  we  had  used  pass,  and if we had IP Forwarding

enabled in our kernel, we would end up having two paths  for

a  packet  to  come  out of, and we would probably panic our

kernel.

It should be noted, however,  that  most  Unix  kernels

(and certainly the ones underlying the systems that ipfilter

usually runs on) have far more efficient routing  code  than

what  exists  in  ipfilter,  and  this keyword should not be

thought of as a way to improve the operating speed  of  your

firewall, and should only be used in places where stealth is

an issue.

4.  NAT and Proxies

Outside  of  the  corporate  environment,  one  of  the

biggest  enticements  of firewall technology to the end user

is the ability to connect several computers through a common

external  interface,  often without the approval, knowledge,

or even consent of their service provider.  To those  famil-

iar  with Linux, this concept is called IP Masquerading, but

to the rest of the world it is known  by  the  more  obscure

name of Network Address Translation, or NAT for short.

-23-

4.1.  Mapping Many Addresses Into One Address

The  basic  use of NAT accomplishes the same thing that

Linux's IP Masquerading function does, and it does  it  with

one simple rule:

map tun0 192.168.1.0/24 -> 20.20.20.1/32

Very  simple.  Whenever a packet goes across the tun0 inter-

face with a source address matching the CIDR network mask of

192.168.1.0/24 (a typical internal address space, since it's

non-routable on the Real  Internet  it  is  often  used  for

internal  networks.    You  should still block these packets

coming in from the outside world  as  in  section  2.)  this

packet  will  be rewritten within the IP stack such that its

source address is 20.20.20.1, and it will be sent on to  its

original destination.   The system also keeps a list of what

translated connections are in progress so that it  can  per-

form  the  reverse  and  remap  the  response (which will be

directed to 20.20.20.1) to the  internal  host  that  really

generated the packet.

There  is  a drawback to the rule we have just written,

though.  In a large number of cases, we  do  not  happen  to

know  what  the  IP address of our outside link is (if we're

using tun0 or ppp0 and a typical ISP) so it makes setting up

our  NAT  tables  a chore.   Luckily, NAT is smart enough to

accept an address of 0/32 as a signal that it  needs  to  go

look  at what the address of that interface really is and we

can rewrite our rule as follows:

map tun0 192.168.1.0/24 -> 0/32

Now we can load our ipnat rules with impunity and connect to

the  outside  world  without having to edit anything. You do

have to run ipf -y to refresh the address if you get discon-

nected and redial, though.

Some of you may be wondering what happens to the source

port when the mapping happens.  With our current  rule,  the

packet's  source port is changed to the first available port

on the NAT host.   There can be instances where  we  do  not

desire this behavior; maybe we have another firewall further

upstream we have to pass through, or perhaps we use the  NAT

host  for  other  things  and we wish to limit the amount of

ports that the NAT system can consume.   ipnat helps us here

too with the portmap keyword:

map tun0 192.168.1.0/24 -> 0/32 portmap tcp/udp 20000:30000

Our rule now shoehorns all the translated connections (which

can be tcp, udp, or tcp/udp) into the port range of 20000 to

30000.

-24-

4.2.  Mapping Many Addresses Into a Pool of Addresses

Another use common use of NAT is to take a small stati-

cally allocated block of addresses and  map  many  computers

into  this  smaller  address space.   This is easy to accom-

plish using what you already know about the map and  portmap

keywords by writing a rule like so:

map tun0 192.168.1.0/24 -> 20.20.20.0/24 portmap tcp/udp 20000:60000

Also,  there  may  be  instances  where a remote application

requires that multiple connections all come from the same IP

address.   We  can help with these situations by telling NAT

to statically map sessions from a  host  into  the  pool  of

addresses  and work some magic to choose a port. This uses a

the keyword map-block as follows:

map-block tun0 192.168.1.0/24 -> 20.20.20.0/24

4.3.  One to One Mappings

Occasionally it is desirable to have a system with  one

IP  address  behind  the  firewall  to appear to have a com-

pletely different IP address.  One example of how this would

work  would be a lab of computers which are then attached to

various networks that are to be put under some kind of test.

In  this  example, you would not want to have to reconfigure

the entire lab when you could place a NAT  system  in  front

and  change  the  addresses in one simple place.   We can do

that with the  bimap  keyword,  for  bidirectional  mapping.

Bimap  has  some  additional  protections  on it to ensure a

known state for the connection, whereas the map  keyword  is

designed  to  allocate  an  address  and  a  source port and

rewrite the packet and go on with life.

bimap tun0 192.168.1.1/32 -> 20.20.20.1/32

will accomplish the mapping for one host.

4.4.  Spoofing Services

Spoofing services?  What does that have to do with any-

thing?    Plenty.   Lets  pretend  that we have a web server

running on 20.20.20.5, and since we've  gotten  increasingly

suspicious  of  our  network  security, we desire to not run

this server on port 80 since that requires a brief  lifespan

as  the  root  user.    But  how  do  we  run  it  on a less

privledged port of 8000 in this world of "anything dot com"?

How will anyone find our server?  We can use the redirection

facilities of NAT to solve this problem by instructing it to

remap  any  connections destined for 20.20.20.5:80 to really

point to 20.20.20.5:8000.   This uses the rdr keyword:

rdr tun0 20.20.20.5 port 80 -> 20.20.20.5 port 8000

-25-

We can also specify the protocol here, if we wanted to redi-

rect  a  UDP service, instead of a TCP service (which is the

default).  For example, if we had a honeypot on our firewall

to  impersonate  the  popular  Back  Orifice for Windows, we

could shovel our entire network into this one place  with  a

simple rule:

rdr tun0 20.20.20.0/24 port 31337 -> 127.0.0.1 port 31337 udp

4.5.  Transparent Proxy Support; Redirection Made Useful

Since  you're  installing  a  firewall,  you  may  have

decided that it is prudent to use a proxy for many  of  your

outgoing  connections  so  that you can further tighten your

filter rules protecting your internal network,  or  you  may

have  run into a situation that the NAT mapping process does

not currently handle properly.   This  can  also  be  accom-

plished with a redirection statement:

rdr xl0 0.0.0.0/0 port 21 -> 127.0.0.1 port 21

This  statement  says  that  any packet coming in on the xl0

interface destined for any address (0.0.0.0/0)  on  the  ftp

port  should be rewritten to connect it with a proxy that is

running on the NAT system on port 21.

This specific example of FTP proxying does lead to some

complications  when  used  with  web browsers or other auto-

matic-login type clients that are unaware  of  the  require-

ments  of  communicating  with the proxy.  There are patches

for TIS Firewall Toolkit'sftp-gw to mate  it  with  the  nat

process so that it can determine where you were trying to go

and automatically send you there.  Many proxy  packages  now

work  in a transparent proxy environment (Squid for example,

located at http://squid.nlanr.net, works fine.)

This application of the rdr keyword is often more  use-

ful  when you wish to force users to authenticate themselves

with the proxy. (For example, you desire your  engineers  to

be  able to surf the web, but you would rather not have your

call-center staff doing so.)

4.6.  Magic Hidden Within NAT; Application Proxies

Since ipnat provides a method  to  rewrite  packets  as

they traverse the firewall, it becomes a convenient place to

build in some application level proxies to make up for  well

known  deficiencies  of  that  application and typical fire-

walls.  For example; FTP.   We can  make  our  firewall  pay

attention to the packets going across it and when it notices

that it's dealing with an Active FTP session, it  can  write

itself  some  temporary  rules,  much like what happens with

keep state, so that the FTP data connection works.    To  do

this, we use a rule like so:

-26-

map tun0 192.168.1.0/24 -> 20.20.20.1/32 proxy port ftp ftp/tcp

You must always remember to place this proxy rule before any

portmap rules, otherwise when portmap comes along and messes

around  with  the packet, the ftp proxy won't notice the ftp

connection, and you'll get errors.

There also exist proxies for "rcmd" (which  we  suspect

is  berkeley  r-* commands which should be forbidden anyway,

thus we haven't looked at what this proxy does) and "raudio"

for  Real  Audio PNM streams.  Likewise, both of these rules

should be put before any portmap rules, if you're doing NAT.

5.  Loading and Manipulating Filter Rules; The ipf Utility

IP  Filter  rules  are loaded by using the ipf utility.

The filter rules can be stored in any file  on  the  system,

but  typically  these  rules  are  stored in /etc/ipf.rules,

/usr/local/etc/ipf.rules, or /etc/opt/ipf/ipf.rules.

IP Filter has two sets of rules, the active set and the

inactive  set.   By default, all operations are performed on

the active set.  You can  manipulate  the  inactive  set  by

adding  -I  to  the  ipf command line.   The two sets can be

toggled by using the -s command line option.  This  is  very

useful  for testing new rule sets without wiping out the old

rule set.

Rules can also be removed  from  the  list  instead  of

added  by using the -r command line option, but it is gener-

ally a safer idea to flush the rule set that you're  working

on with -F and completely reload it when making changes.

In  summary,  the easiest way to load a rule set is ipf

-Fa -f /etc/ipf.rules.  For more  complicated  manipulations

of the rule set, please see the ipf(1) man page.

6.  Loading and Manipulating NAT Rules; The ipnat Utility

NAT  rules  are loaded by using the ipnat utility.  The

NAT rules can be stored in any file on the system, but typi-

cally   these   rules   are   stored   in  /etc/ipnat.rules,

/usr/local/etc/ipnat.rules, or /etc/opt/ipf/ipnat.rules.

Rules can also be removed  from  the  list  instead  of

added  by using the -r command line option, but it is gener-

ally a safer idea to flush the rule set that you're  working

on  with  -C  and  completely reload it when making changes.

Any active mappings are not  affected  by  -C,  and  can  be

removed with -F.

-27-

NAT  rules and active mappings can be examined with the

-l command line option.

In summary, the easiest way to load a NAT rule  set  is

ipnat -CF -f /etc/ipnat.rules.

7.  Monitoring and Debugging

There  will come a time when you are interested in what

your firewall is  actually  doing,  and  ipfilter  would  be

incomplete if it didn't have a full suite of status monitor-

ing tools.

7.1.  The ipfstat utility

In its simplest  form,  ipfstat  displays  a  table  of

interesting data about how your firewall is performing, such

as how many packets have been passed  or  blocked,  if  they

were  logged  or not, how many state entries have been made,

and so on.  Here's an example of  something  you  might  see

from running the tool:

# ipfstat

input packets:         blocked 99286 passed 1255609 nomatch 14686 counted 0

output packets:         blocked 4200 passed 1284345 nomatch 14687 counted 0

input packets logged:  blocked 99286 passed 0

output packets logged:  blocked 0 passed 0

packets logged:        input 0 output 0

log failures:          input 3898 output 0

fragment state(in):     kept 0  lost 0

fragment state(out):    kept 0  lost 0

packet state(in):       kept 169364     lost 0

packet state(out):      kept 431395     lost 0

ICMP replies:   0       TCP RSTs sent:  0

Result cache hits(in):  1215208 (out):  1098963

IN Pullups succeeded:   2       failed: 0

OUT Pullups succeeded:  0       failed: 0

Fastroute successes:    0       failures:       0

TCP cksum fails(in):    0       (out):  0

Packet log flags set: (0)

none

ipfstat  is  also  capable  of showing you your current rule

list.  Using the -i or the -o flag will show  the  currently

loaded  rules  for  in or out, respectively.  Adding a -h to

this will provide more useful information at the  same  time

by showing you a "hit count" on each rule.  For example:

# ipfstat -ho

2451423 pass out on xl0 from any to any

354727 block out on ppp0 from any to any

430918 pass out quick on ppp0 proto tcp/udp from 20.20.20.0/24 to any keep state keep frags

-28-

From  this, we can see that perhaps there's something abnor-

mal going on, since we've got a lot of blocked packets  out-

bound, even with a very permissive pass out rule.  Something

here may warrant further investigation,  or it may be  func-

tioning perfectly by design.  ipfstat can't tell you if your

rules are right or wrong, it can only tell you what is  hap-

pening because of your rules.

To  further  debug  your  rules,  you may want to use the -n

flag, which will show the rule number next to each rule.

# ipfstat -on

@1 pass out on xl0 from any to any

@2 block out on ppp0 from any to any

@3 pass out quick on ppp0 proto tcp/udp from 20.20.20.0/24 to any keep state keep frags

The final piece of really interesting information that ipfs-

tat  can  provide  us is a dump of the state table.  This is

done with the -s flag:

# ipfstat -s

281458 TCP

319349 UDP

0 ICMP

19780145 hits

5723648 misses

0 maximum

0 no memory

1 active

319349 expired

281419 closed

100.100.100.1 -> 20.20.20.1 ttl 864000 pass 20490 pr 6 state 4/4

pkts 196 bytes 17394    987 -> 22 585538471:2213225493 16592:16500

pass in log quick keep state

pkt_flags & b = 2,              pkt_options & ffffffff = 0

pkt_security & ffff = 0, pkt_auth & ffff = 0

Here we see that we have one state entry for a  TCP  connec-

tion.   The  output  will vary slightly from version to ver-

sion, but the basic information is the same.  We can see  in

this  connection that we have a fully established connection

(represented by the 4/4 state.  Other states are  incomplete

and  will  be  documented fully later.)  We can see that the

state entry has a time to live of 240  hours,  which  is  an

absurdly  long  time,  but is the default for an established

TCP connection.   This TTL counter is decremented every sec-

ond  that  the  state  entry  is  not used, and will finally

result in the connection being purged if it  has  been  left

idle.    The  TTL is also reset to 864000 whenever the state

IS used, ensuring that the entry will not time out while  it

is being actively used.  We can also see that we have passed

196 packets consisting of about 17kB worth of data over this

connection.   We  can  see  the ports for both endpoints, in

this case 987 and 22; which  means  that  this  state  entry

-29-

represents  a  connection  from  100.100.100.1  port  987 to

20.20.20.1 port 22.   The really big numbers in  the  second

line are the TCP sequence numbers for this connection, which

helps to ensure that someone isn't easily able to  inject  a

forged  packet  into  your  session.  The TCP window is also

shown.   The third line is a synopsis of the  implicit  rule

that was generated by the keep state code, showing that this

connection is an inbound connection.

7.2.  The ipmon utility

ipfstat is great for  collecting  snapshots  of  what's

going  on  on  the system, but it's often handy to have some

kind of log to look at and watch events as  they  happen  in

time.    ipmon  is  this tool.  ipmon is capable of watching

the packet log (as created with  the  log  keyword  in  your

rules), the state log, or the nat log, or any combination of

the three.   This tool can either be run in the  foreground,

or as a daemon which logs to syslog or a file.  If we wanted

to watch the state table in action, ipmon -o  S  would  show

this:

# ipmon -o S

01/08/1999 15:58:57.836053 STATE:NEW 100.100.100.1,53 -> 20.20.20.15,53 PR udp

01/08/1999 15:58:58.030815 STATE:NEW 20.20.20.15,123 -> 128.167.1.69,123 PR udp

01/08/1999 15:59:18.032174 STATE:NEW 20.20.20.15,123 -> 128.173.14.71,123 PR udp

01/08/1999 15:59:24.570107 STATE:EXPIRE 100.100.100.1,53 -> 20.20.20.15,53 PR udp Pkts 4 Bytes 356

01/08/1999 16:03:51.754867 STATE:NEW 20.20.20.13,1019 -> 100.100.100.10,22 PR tcp

01/08/1999 16:04:03.070127 STATE:EXPIRE 20.20.20.13,1019 -> 100.100.100.10,22 PR tcp Pkts 63 Bytes 4604

Here  we  see  a state entry for an external dns request off

our nameserver, two xntp pings to well-known  time  servers,

and a very short lived outbound ssh connection.

ipmon  is  also capable of showing us what packets have

been logged.  For example, when using  state,  you'll  often

run into packets like this:

# ipmon -o I

15:57:33.803147 ppp0 @0:2 b 100.100.100.103,443 -> 20.20.20.10,4923 PR tcp len 20 1488 -A

What  does  this  mean?   The first field is obvious, it's a

timestamp.  The second field is also  pretty  obvious,  it's

the  interface that this event happened on.  The third field

@0:2 is something most people miss. This is  the  rule  that

caused  the  event to happen.  Remember ipfstat -in?  If you

wanted to know where this came from, you  could  look  there

for  rule  2  in rule group 0.  The fourth field, the little

"b" says that this packet was blocked, and you'll  generally

ignore  this  unless  you're logging passed packets as well,

which would be a little "p" instead.  The  fifth  and  sixth

fields  are  pretty  self-explanatory,  they  say where this

packet came from and where it was going. The seventh  ("PR")

and  eighth fields tell you the protocol and the ninth field

-30-

tells you the size of the packet.  The last part,  the  "-A"

in  this  case, tells you the flags that were on the packet;

This one was an ACK packet.  Why did I  mention  state  ear-

lier?   Due to the often laggy nature of the Internet, some-

times packets will be regenerated.   Sometimes,  you'll  get

two  copies  of  the  same packet, and your state rule which

keeps track of sequence numbers will have already seen  this

packet,  so it will assume that the packet is part of a dif-

ferent connection.   Eventually this packet will run into  a

real  rule and have to be dealt with.   You'll often see the

last packet of a session being closed get logged because the

keep  state code has already torn down the connection before

the last packet has had a chance to make it  to  your  fire-

wall.   This  is normal, do not be alarmed.  Another example

packet that might be logged:

12:46:12.470951 xl0 @0:1 S 20.20.20.254 -> 255.255.255.255 PR icmp len 20 9216 icmp 9/0

This is a ICMP router discovery broadcast.  We can  tell  by

the ICMP type 9/0.

Finally, ipmon also lets us look at the NAT table in action.

# ipmon -o N

01/08/1999 05:30:02.466114 @2 NAT:RDR 20.20.20.253,113 <- -> 20.20.20.253,113 [100.100.100.13,45816]

01/08/1999 05:30:31.990037 @2 NAT:EXPIRE 20.20.20.253,113 <- -> 20.20.20.253,113 [100.100.100.13,45816] Pkts 10 Bytes 455

This would be a redirection to an identd that lies  to  pro-

vide  ident service for the hosts behind our NAT, since they

are typically unable to provide this service for  themselves

with ordinary natting.

8.   Specific  Applications of IP Filter - Things that don't

fit, but should be mentioned anyway.

8.1.  Keep State With Servers and Flags.

Keeping state is a good thing, but it's quite  easy  to

make  a mistake in the direction that you want to keep state

in.   Generally, you want to have a keep  state  keyword  on

the  first rule that interacts with a packet for the connec-

tion. One common mistake that  is  made  when  mixing  state

tracking with filtering on flags is this:

-----------

For  a  technical  presentation of the IP Filter

stateful inspection engine, please see  the  white

paper  Real  Stateful  TCP  Packet Filtering in IP

Filter, by Guido van Rooij.   This  paper  may  be

found                                           at

<http://www.iae.nl/users/guido/papers/tcp_filter-

ing.ps.gz>

-31-

block in all

pass in quick proto tcp from any to 20.20.20.20/32 port = 23 flags S

pass out all keep state

That  certainly  appears to allow a connection to be created

to the telnet server on 20.20.20.20, and the replies  to  go

back.   If  you try using this rule, you'll see that it does

work--Momentarily.  Since we're filtering for the SYN  flag,

the  state entry never fully gets completed, and the default

time to live for an incomplete state is 60 seconds.

We can solve this by rewriting the rules in one of two ways:

1)

block in all

pass in quick proto tcp from any to 20.20.20.20/32 port = 23 keep state

block out all

or:

2)

block in all

pass in quick proto tcp from any to 20.20.20.20/32 port = 23 flags S keep state

pass out all keep state

Either  of these sets of rules will result in a fully estab-

lished state entry for a connection to your server.

8.2.  Coping With FTP

FTP is one of those protocols that you just have to sit

back  and  ask  "What the heck were they thinking?"  FTP has

many problems that the firewall administrator needs to  deal

with.   What's  worse,  the  problems the administrator must

face are different between making ftp clients work and  mak-

ing ftp servers work.

Within  the  FTP  protocol, there are two forms of data

transfer, called active and passive.  Active  transfers  are

those  where  the  server  connects  to  an open port on the

client to send  data.   Conversely,  passive  transfers  are

those  where  the  client  connects to the server to recieve

data.

8.2.1.  Running an FTP Server

In running an FTP server, handling Active FTP  sessions

is  easy  to  setup.  At the same time, handling Passive FTP

sessions is a big problem.  First we'll cover how to  handle

Active FTP, then move on to Passive.  Generally, we can han-

dle Active FTP sessions like we would an  incoming  HTTP  or

SMTP  connection;  just open the ftp port and let keep state

-32-

do the rest:

pass in quick proto tcp from any to 20.20.20.20/32 port = 21 flags S keep state

pass out proto tcp all keep state

These rules will allow Active FTP sessions, the most  common

type, to your ftp server on 20.20.20.20.

The next challenge becomes handling Passive FTP connec-

tions.  Web browsers default to this mode, so it's  becoming

quite popular and as such it should be supported.  The prob-

lem with passive connections are that for every passive con-

nection,  the server starts listening on a new port (usually

above 1023).   This  is  essentially  like  creating  a  new

unknown  service  on  the  server.   Assuming we have a good

firewall with a default-deny policy, that new  service  will

be  blocked, and thus Active FTP sessions are broken.  Don't

despair!  There's hope yet to be had.

A person's first inclination to  solving  this  problem

might  be  to  just open up all ports above 1023.  In truth,

this will work:

pass in quick proto tcp from any to 20.20.20.20/32 port > 1023 flags S keep state

pass out proto tcp all keep state

This is somewhat unsatisfactory, though.  By letting  every-

thing  above  1023  in,  we actually open ourselves up for a

number of potential problems.  While 1-1023  is  the  desig-

nated  area  for  server  services to run, numerous programs

decided to use numbers higher than 1023, such as nfsd and X.

The  good  news  is that your FTP server gets to decide

which ports get assigned to  active  sessions.   This  means

that  instead of opening all ports above 1023, you can allo-

cate ports 15001-19999 as ftp ports and only open that range

of your firewall up.  In wu-ftpd, this is done with the pas-

sive ports option in ftpaccess.  Please see the man page  on

ftpaccess  for  details  in  wu-ftpd  configuration.  On the

ipfilter side, all we need do is setup corresponding rules:

pass in quick proto tcp from any to 20.20.20.20/32 port 15000 >< 20000 flags S keep state

pass out proto tcp all keep state

If even this solution doesn't satisfy you,  you  can  always

hack IPF support into your FTP server, or FTP server support

into IPF.

8.2.2.  Running an FTP Client

While FTP server support is still less than perfect  in

IPF,  FTP  client support has been working well since 3.3.3.

As with FTP servers, there  are  two  types  of  ftp  client

transfers: passive and active.

-33-

The  simplest  type  of  client transfer from the fire-

wall's standpoint is the passive transfer.  Assuming  you're

keeping  state  on all outbound tcp sessions, passive trans-

fers will work already.  If you're not doing  this  already,

please consider the following:

pass out proto tcp all keep state

The  second  type  of client transfer, active, is a bit more

troublesome,  but  nonetheless  a  solved  problem.   Active

transfers  cause  the  server to open up a second connection

back to the client for data to flow through.  This  is  nor-

mally a problem when there's a firewall in the middle, stop-

ping outside connections from  coming  back  in.   To  solve

this,  ipfilter  includes  an  ipnat proxy which temporarily

opens up a hole in the firewall just for the FTP  server  to

get  back  to the client.  Even if you're not using ipnat to

do nat, the proxy is still effective.  The  following  rules

is  the  bare minimum to add to the ipnat configuration file

(ep0 should be the interface name of  the  outbound  network

connection):

map ep0 0/0 -> 0/32 proxy port 21 ftp/tcp

For more details on ipfilter's internal proxies, see section

3.6

8.3.  Assorted Kernel Variables

There are some useful kernel tunes that either need  to

be  set  for ipf to function, or are just generally handy to

know about for building firewalls.  The first major one  you

must  set  is to enable IP Forwarding, otherwise ipf will do

very little, as the underlying ip stack won't actually route

packets.

IP Forwarding:

openbsd:

net.inet.ip.forwarding=1

freebsd:

net.inet.ip.forwarding=1

solaris:

ndd -set /dev/ip ip_forwarding 1

Ephemeral Port Adjustment:

openbsd:

net.inet.ip.portfirst = 25000

-34-

freebsd:

net.inet.ip.portrange.first  =  25000  net.inet.ip.por-

trange.last = 49151

solaris:

ndd -set /dev/tcp tcp_smallest_anon_port 25000

ndd -set /dev/tcp tcp_largest_anon_port 65535

Other Useful Values:

openbsd:

net.inet.ip.sourceroute = 0

net.inet.ip.directed-broadcast = 0

freebsd:

net.inet.ip.sourceroute=0

net.ip.accept_sourceroute=0

solaris:

ndd -set /dev/ip ip_forward_directed_broadcasts 0

ndd -set /dev/ip ip_forward_src_routed 0

ndd -set /dev/ip ip_respond_to_echo_broadcast 0

In addition, freebsd has some ipf specific sysctl variables.

net.inet.ipf.fr_flags: 0

net.inet.ipf.fr_pass: 514

net.inet.ipf.fr_active: 0

net.inet.ipf.fr_tcpidletimeout: 864000

net.inet.ipf.fr_tcpclosewait: 60

net.inet.ipf.fr_tcplastack: 20

net.inet.ipf.fr_tcptimeout: 120

net.inet.ipf.fr_tcpclosed: 1

net.inet.ipf.fr_udptimeout: 120

net.inet.ipf.fr_icmptimeout: 120

net.inet.ipf.fr_defnatage: 1200

net.inet.ipf.fr_ipfrttl: 120

net.inet.ipf.ipl_unreach: 13

net.inet.ipf.ipl_inited: 1

net.inet.ipf.fr_authsize: 32

net.inet.ipf.fr_authused: 0

net.inet.ipf.fr_defaultauthage: 600

9.  Fun with ipf!

This section doesn't necessarily teach you anything new

about ipf, but it may raise an issue or two that you haven't

yet  thought  up  on your own, or tickle your brain in a way

-35-

that  you  invent  something  interesting  that  we  haven't

thought of.

9.1.  Localhost Filtering

A  long  time ago at a university far, far away, Weitse

Venema created the tcp-wrapper package, and ever since, it's

been  used  to add a layer of protection to network services

all over the world.  This is good.  But,  tcp-wrappers  have

flaws.  For starters, they only protect TCP services, as the

name suggests.   Also, unless  you  run  your  service  from

inetd, or you have specifically compiled it with libwrap and

the appropriate hooks, your service isn't protected.    This

leaves  gigantic  holes in your host security.   We can plug

these up by using ipf on the local host.   For  example,  my

laptop  often gets plugged into or dialed into networks that

I don't specifically trust, and so, I use the following rule

set:

pass in quick on lo0 all

pass out quick on lo0 all

block in log all

block out all

pass in quick proto tcp from any to any port = 113 flags S keep state

pass in quick proto tcp from any to any port = 22 flags S keep state

pass in quick proto tcp from any port = 20 to any port 39999 >< 45000 flags S keep state

pass out quick proto icmp from any to any keep state

pass out quick proto tcp/udp from any to any keep state keep frags

It's  been  like  that for quite a while, and I haven't suf-

fered any pain or anguish as a result of having  ipf  loaded

up all the time.  If I wanted to tighten it up more, I could

switch to using the NAT ftp proxy and I could  add  in  some

rules to prevent spoofing.   But even as it stands now, this

box is far more restrictive about what it  presents  to  the

local  network and beyond than the typical host does.   This

is a good thing if you happen to run a machine that allows a

lot  of  users on it, and you want to make sure  one of them

doesn't happen to start up a service  they  wern't  supposed

to.   It won't stop a malicious hacker with root access from

adjusting your ipf rules and starting a service anyway,  but

it  will keep the "honest" folks honest, and your weird ser-

vices safe, cozy and warm even on a malicious  LAN.   A  big

win, in my opinion.   Using local host filtering in addition

to a somewhat less-restrictive "main firewall"  machine  can

solve  many  performance  issues as well as political night-

mares like "Why doesn't ICQ work?" and "Why can't  I  put  a

web  server  on  my  own workstation! It's MY WORKSTATION!!"

Another very big win.  Who says you can't have security  and

convienence at the same time?

-36-

9.2.  What Firewall?  Transparent filtering.

One  major  concern  in  setting  up  a firewall is the

integrity of the firewall itself.  Can somebody  break  into

your  firewall,  thereby  subverting its ruleset?  This is a

common problem administrators must face,  particularly  when

they're  using  firewall  solutions  on top of their Unix/NT

machines.  Some use it as an arguement for blackbox hardware

solutions,  under  the flawed notion that inherant obscurity

of their closed system increases their security.  We have  a

better way.

Many network admins are familiar with the common ether-

net bridge.  This is a device  that  connects  two  separate

ethernet  segments  to make them one.  An ethernet bridge is

typically used to connect separate buildings, switch network

speeds,  and extend maximum wire lengths.  Hubs and switches

are common bridges, sometimes they're just 2 ported  devices

called   repeaters.   Recent  versions  of  Linux,  OpenBSD,

NetBSD, and FreeBSD include code to convert $1000  PCs  into

$10  bridges,  too!  What all bridges tend to have in common

is that though they  sit  in  the  middle  of  a  connection

between two machines, the two machines don't know the bridge

is there.  Enter ipfilter and OpenBSD.

Ethernet bridging takes place  at  Layer2  on  the  ISO

stack.   IP  takes  place on Layer3.  IP Filter in primarily

concerned with Layer3, but dabbles in Layer2 by working with

interfaces.   By  mixing  IP  filter  with  OpenBSD's bridge

device, we can create a firewall that is both invisible  and

unreachable.   The  system  needs  no IP address, it doesn't

even need to reveal its ethernet address.  The only telltale

sign that the filter might be there is that latency is some-

what higher than a piece of cat5 would normally make it, and

that  packets  don't seem to make it to their final destina-

tion.

The setup for this sort of ruleset is surprisingly sim-

ple,  too.   In  OpenBSD,  the  first bridge device is named

bridge0.  Say we have two ethernet cards in our  machine  as

well,  xl0 and xl1.  To turn this machine into a bridge, all

one need do is enter the following three commands:

brconfig bridge0 add xl0 add xl1 up

ifconfig xl0 up

ifconfig xl1 up

At ths point, all traffic ariving on xl0 is sent out xl1 and

all  traffic  on xl1 is sent out xl0.  You'll note that nei-

ther interface has been assigned an IP address,  nor  do  we

need assign one.  All things considered, it's likely best we

not add one at all.

-37-

Rulesets behave essentially the  as  the  always  have.

Though  there  is a bridge0 interface, we don't filter based

on it.  Rules continue  to  be  based  upon  the  particular

interface  we're  using,  making  it important which network

cable is plugged into which network card in the back of  the

machine.  Lets start with some basic filtering to illistrate

what's happened.  Assume the network used to look like this:

20.20.20.1 <---------------------------------> 20.20.20.0/24 network hub

That  is,  we  have  a router at 20.20.20.1 connected to the

20.20.20.0/24 network.  All packets from  the  20.20.20.0/24

network  go  through  20.20.20.1 to get to the outside world

and vice versa.  Now we add the Ipf Bridge:

20.20.20.1 <-------/xl0 IpfBridge xl1/-------> 20.20.20.0/24 network hub

We also have the following ruleset loaded on  the  IpfBridge

host:

pass in  quick  all

pass out quick  all

With  this ruleset loaded, the network is functionally iden-

tical.  As far as the 20.20.20.1 router is concerned, and as

far  as  the 20.20.20.0/24 hosts are concerned, the two net-

work diagrams are identical.  Now lets  change  the  ruleset

some:

block in quick on xl0 proto icmp

pass  in  quick all

pass  out quick all

Still,  20.20.20.1  and  20.20.20.0/24  think the network is

identical, but if 20.20.20.1 attempts to ping 20.20.20.2, it

will  never get a reply.  What's more, 20.20.20.2 won't even

get the packet in the first place.  IPfilter will  intercept

the  packet before it even gets to the other end of the vir-

tual wire.  We can put a  bridged  filter  anywhere.   Using

this  method  we can shrink the network trust circle down an

individual host level (given enough ethernet cards:-)

Blocking icmp from the world seems kind of silly, espe-

cially  if  you're a sysadmin and like pinging the world, to

traceroute, or to resize your MTU.  Lets construct a  better

ruleset  and  take  advantage of the original key feature of

ipf: stateful inspection.

pass  in quick on xl1 proto tcp  keep state

pass  in quick on xl1 proto udp  keep state

pass  in quick on xl1 proto icmp keep state

block in quick on xl0

-38-

In this situation, the 20.20.20.0/24 network  (perhaps  more

aptly  called  the  xl1  network)  can now reach the outside

world, but the outside world can't reach it,  and  it  can't

figure out why, either.  The router is accessible, the hosts

are active, but the outside world just can't get  in.   Even

if  the  router  itself were compromised, the firewall would

still be active and successful.

So far, we've been filtering by interface and  protocol

only.   Even  though  bridging  is  concerned layer2, we can

still discriminate based on IP address.  Normally we have  a

few services running, so our ruleset may look like this:

pass  in quick on xl1 proto tcp  keep state

pass  in quick on xl1 proto udp  keep state

pass  in quick on xl1 proto icmp keep state

block in quick on xl1 # nuh-uh, we're only passing tcp/udp/icmp sir.

pass  in quick on xl0 proto udp from any to 20.20.20.2/32 port=53 keep state

pass  in quick on xl0 proto tcp from any to 20.20.20.2/32 port=53 flags S keep state

pass  in quick on xl0 proto tcp from any to 20.20.20.3/32 port=25 flags S keep state

pass  in quick on xl0 proto tcp from any to 20.20.20.7/32 port=80 flags S keep state

block in quick on xl0

Now  we  have  a  network where 20.20.20.2 is a zone serving

name server, 20.20.20.3 is  an  incoming  mail  server,  and

20.20.20.7 is a web server.

Bridged  IP Filter is not yet perfect, we must confess.

You'll note that all the rules are setup using the in direc-

tion  instead  of  a  combination  of  in  and out.  This is

because the out direction seems presently broken with bridg-

ing in OpenBSD.  Using IP Filter with bridging makes the use

of IPF's NAT features inadvisable, if not downright  danger-

ous.   The  first  problem  is  that it would give away that

there's a filtering bridge.  The  second  problem  would  be

that  the bridge has no IP address to masquerade with, which

will most assuredly lead to confusion and perhaps  a  kernel

panic to boot.

9.2.1.   Using  Transparent  Filtering to Fix Network Design

Mistakes

Many organizations started using IP  well  before  they

thought  a  firewall  or a subnet would be a good idea.  Now

they have class-C sized networks or larger that include  all

their  servers,  their  workstations,  their routers, coffee

makers, everything.  The horror!  Renumbering  with  propper

subnets, trust levels, filters, and so are in both time con-

suming and expensive.  The expense in hardware and man hours

alone  is  enough  to  make  most organizations unwilling to

really solve  the  problem,  not  to  mention  the  downtime

involved.  The typical problem network looks like this:

20.20.20.1   router               20.20.20.6   unix server

-39-

20.20.20.2   unix server          20.20.20.7   nt workstation

20.20.20.3   unix server          20.20.20.8   nt server

20.20.20.4   win98 workstation    20.20.20.9   unix workstation

20.20.20.5   intelligent switch   20.20.20.10  win95 workstation

Only  it's  about 20 times larger and messier and frequently

undocumented.  Ideally, you'd have all the trusting  servers

in  one  subnet,  all the work- stations in another, and the

network switches in a third.  Then the router  would  filter

packets between the subnets, giving the workstations limited

access to the servers, nothing access to the  switches,  and

only  the  sysadmin's  workstation access to the coffee pot.

I've never seen a class-C sized network with such coherancy.

IP Filter can help.

To  start with, we're going to separate the router, the

workstations, and the servers.  To do this  we're  going  to

need  2  hubs  (or switches) which we probably already have,

and an IPF machine with 3 ethernet cards.   We're  going  to

put  all  the servers on one hub and all the workstations on

the other.  Normally we'd then  connect  the  hubs  to  each

other, then to the router.  Instead, we're going to plug the

router into IPF's xl0 interface, the servers into IPF's  xl1

interface,  and  the  workstations into IPF's xl2 interface.

Our network diagram looks something like this:

| 20.20.20.2  unix server

router (20.20.20.1)              ____________| 20.20.20.3  unix server

|                              /            | 20.20.20.6  unix server

|                             /xl1          | 20.20.20.7  nt server

------------/xl0 IPF Bridge <

xl2         | 20.20.20.4  win98 workstation

____________| 20.20.20.8  nt workstation

| 20.20.20.9  unix workstation

| 20.20.20.10 win95 workstation

Where once there was nothing but interconnecting wires,  now

there's  a  filtering bridge that not a single host needs to

be modified to take advantage of.  Presumably we've  already

enabled  bridging  so the network is behaving perfectly nor-

mally.  Further, we're starting off with a ruleset much like

our last ruleset:

pass  in quick on xl0 proto udp from any to 20.20.20.2/32 port=53 keep state

pass  in quick on xl0 proto tcp from any to 20.20.20.2/32 port=53 flags S keep state

pass  in quick on xl0 proto tcp from any to 20.20.20.3/32 port=25 flags S keep state

pass  in quick on xl0 proto tcp from any to 20.20.20.7/32 port=80 flags S keep state

block in quick on xl0

pass  in quick on xl1 proto tcp  keep state

pass  in quick on xl1 proto udp  keep state

pass  in quick on xl1 proto icmp keep state

block in quick on xl1 # nuh-uh, we're only passing tcp/udp/icmp sir.

pass  in quick on xl2 proto tcp  keep state

pass  in quick on xl2 proto udp  keep state

-40-

pass  in quick on xl2 proto icmp keep state

block in quick on xl2 # nuh-uh, we're only passing tcp/udp/icmp sir.

Once  again, traffic coming from the router is restricted to

DNS, SMTP, and HTTP.  At the moment,  the  servers  and  the

workstations can exchange traffic freely.  Depending on what

kind of organization you are, there might be something about

this network dynamic you don't like.  Perhaps you don't want

your workstations getting access to  your  servers  at  all?

Take the xl2 ruleset of:

pass  in quick on xl2 proto tcp  keep state

pass  in quick on xl2 proto udp  keep state

pass  in quick on xl2 proto icmp keep state

block in quick on xl2 # nuh-uh, we're only passing tcp/udp/icmp sir.

And change it to:

block in quick on xl2 from any to 20.20.20.0/24

pass  in quick on xl2 proto tcp  keep state

pass  in quick on xl2 proto udp  keep state

pass  in quick on xl2 proto icmp keep state

block in quick on xl2 # nuh-uh, we're only passing tcp/udp/icmp sir.

Perhaps  you want them to just get to the servers to get and

send their mail with IMAP?  Easily done:

pass  in quick on xl2 proto tcp from any to 20.20.20.3/32 port=25

pass  in quick on xl2 proto tcp from any to 20.20.20.3/32 port=143

block in quick on xl2 from any to 20.20.20.0/24

pass  in quick on xl2 proto tcp  keep state

pass  in quick on xl2 proto udp  keep state

pass  in quick on xl2 proto icmp keep state

block in quick on xl2 # nuh-uh, we're only passing tcp/udp/icmp sir.

Now your workstations and servers  are  protected  from  the

outside world, and the servers are protected from your work-

stations.

Perhaps the opposite is true, maybe you want your work-

stations  to be able to get to the servers, but not the out-

side world.  After all, the next generation of  exploits  is

breaking  the clients, not the servers.  In this case, you'd

change the xl2 rules to look more like this:

pass  in quick on xl2 from any to 20.20.20.0/24

block in quick on xl2

Now the servers have free reign, but the  clients  can  only

connect  to  the  servers.  We might want to batten down the

hatches on the servers, too:

pass  in quick on xl1 from any to 20.20.20.0/24

block in quick on xl1

-41-

With the combination of these two, the clients  and  servers

can  talk  to each other, but neither can access the outside

world (though the outside world can get to the few  services

from  earlier).  The whole ruleset would look something like

this:

pass  in quick on xl0 proto udp from any to 20.20.20.2/32 port=53 keep state

pass  in quick on xl0 proto tcp from any to 20.20.20.2/32 port=53                                                              flags S keep state

pass  in quick on xl0 proto tcp from any to 20.20.20.3/32 port=25                                                              flags S keep state

pass  in quick on xl0 proto tcp from any to 20.20.20.7/32 port=80                                                              flags S keep state

block in quick on xl0

pass  in quick on xl1 from any to 20.20.20.0/24

block in quick on xl1

pass  in quick on xl2 from any to 20.20.20.0/24

block in quick on xl2

So remember, when your  network  is  a  mess  of  twisty  IP

addresses  and machine classes, transparent filtered bridges

can solve a problem that would otherwise be lived  with  and

perhaps someday exploited.

9.3.  Drop-Safe Logging With dup-to and to.

Until now, we've been using the filter to drop packets.

Instead of dropping them, lets consider passing them  on  to

another system that can do something useful with this infor-

mation beyond the logging we can perform with  ipmon.    Our

firewall  system,  be  it  a bridge or a router, can have as

many interfaces as we can cram into the system.  We can  use

this information to create a "drop-safe" for our packets.  A

good example of a use for this  would  be  to  implement  an

intrusion  detection  network.   For  starters,  it might be

desirable to hide the presence of  our  intrusion  detection

systems  from our real network so that we can keep them from

being detected.

Before we get started, there are some operational char-

acteristics  that  we  need to make note of.  If we are only

going to deal with blocked packets, we can use either the to

keyword  or  the fastroute keyword. (We'll cover the differ-

ences between these two later)  If we're going to  pass  the

packets  like  we  normally would, we need to make a copy of

the packet for our drop-safe log with the dup-to keyword.

9.3.1.  The dup-to Method

If, for example, we wanted to send a copy of everything

going  out the xl3 interface off to our drop-safe network on

ed0, we would use this rule in our filter list:

pass out on xl3 dup-to ed0 from any to any

You might also have a need to send the packet directly to  a

specific  IP  address  on  your drop-safe network instead of

-42-

just making a copy of the packet out there  and  hoping  for

the best.  To do this, we modify our rule slightly:

pass out on xl3 dup-to ed0:192.168.254.2 from any to any

But  be  warned  that  this  method  will  alter  the copied

packet's destination address, and may thus destroy the  use-

fulness  of  the  log.   For  this reason, we reccomend only

using the known address method of logging when  you  can  be

certain  that the address that you're logging to corresponds

in some way to what you're  logging  for  (e.g.:  don't  use

"192.168.254.2"  for  logging  for  both your web server and

your mail server, since you'll have a hard time later trying

to  figure out which system was the target of a specific set

of packets.)

This technique can be used  quite  effectively  if  you

treat  an  IP  Address on your drop-safe network in much the

same way that you would treat a Multicast Group on the  real

internet.  (e.g.:  "192.168.254.2"  could be the channel for

your http traffic analysis system,  "23.23.23.23"  could  be

your  channel  for telnet sessions, and so on.)    You don't

even need to actually have this address set as an address or

alias  on  any  of  your  analysis  systems.  Normally, your

ipfilter machine would need to ARP for the  new  destination

address  (using  dup-to  ed0:192.168.254.2 style, of course)

but we can avoid that issue by creating a static  arp  entry

for this "channel" on our ipfilter system.

In  general, though, dup-to ed0 is all that is required

to get a new copy of the packet over to our  drop-safe  net-

work for logging and examination.

9.3.2.  The to Method

The  dup-to  method  does  have  an immediate drawback,

though.  Since it has to make  a  copy  of  the  packet  and

optionally  modify it for its new destination, it's going to

take a while to complete all this work and be ready to  deal

with the next packet coming in to the ipfilter system.

If we don't care about passing the packet to its normal

destination and we were going to block  it  anyway,  we  can

just  use the to keyword to push this packet past the normal

routing table and force it to go out a  different  interface

than it would normally go out.

block in quick on xl0 to ed0 proto tcp from any to any port < 1024

we  use  block  quick for to interface routing, because like

fastroute, the to interface code will  generate  two  packet

paths through ipfilter when used with pass, and likely cause

your system to panic.